## Slide 1
BASIC
THERMODYNAMICS LECTURE - 1
(INTRODUCTION & BASIC CONCEPTS)

## Slide 2
WHAT IS THERMODYNAMICS?
¢ Thermodynamics is branch of science which deals with energy transfer & its effects on properties
(physical & chemical) of the substance.
¢ Amount of heat (or work) transfer taking place while arriving at one state from another is the main
concern in thermodynamics
SYSTEM & SURROUNDINGS
SYSTEM
It is a fixed mass or region in a space (control volume) where our study is focussed.
SURROUNDINGS
Everything external to the system is the surrounding
(That part of the surrounding which is effected by the system is known as the immediate surrounding)

## Slide 3
TYPES OF SYSTEMS
CLOSED SYSTEM
It is a type of system in which onlysenergyanteractions & no mass interactions take place.
Ex. Piston-cylinder arrangement without valves
OPEN SYSTEM
It is a type of system in which bothsenergy:Semassunteractions takes place.
Ex. Piston-cylinder arrangement with valves
ISOLATED SYSTEM
It is a type of system in which neitherenergynormassunteractions takes place.
Ex. Hot coffee or tea kept in a well insulated thermos flask, universe

## Slide 4
BOUNDARY
It is reabor imaginary surface that separates system from the surroundings
It can be fined Qn iovablses MIoVABLE CONTROL
/ Me VOLUME
> : A ,
i "j
- >
Fixed | fa sj
IMAG NARY REAL
BoUNDARY BounDARY

## Slide 5
Key points with respect to Properties
¢ They are poing functions
¢ They are exact differentials
¢ They are independent of past history
STATE
Any condition of the system is known as the state of the system
PROCESS Change of state is called process
PROCESS PATH
The infinite states through which the system passes while going from initial state to the final state is
called as the process path

## Slide 6
CLASSIFICATION OF PROCESSES
> QUASI-STATIC & NON QUASI-STATIC
Quasi-static Process .
¢ It is that kind of a process that occurs infinitely slow
* It is represented by joined lines on property diagrams
Non Quasi-static Process
* It is that kind of a process that does not occurs infinitely slow
* It is represented by dashed lines on property diagrams
>» REVERSIBLE & IRREVERSIBLE
Reversible Process
It is that kind of a process which can be reversed in direction following the same path & without leaving
any effect on the system & the surroundings
Irreversible Process
It is that kind of a process which is not reversible

## Slide 7
Some key points:
¢ All quasi-static processes are nor reversible but a reversible process is always quasi-static
* Quasi-static compression & expansion of a gas is reversible process
MACROSCOPIC & MICROSCOPIC ANALYSIS
Macroscopic Analysis
* In this analysis, average molecular behavior is taken into consideration
¢ This approach is valid till the concept of continuum holds good
(Mean free path of the molecules <<<<<< system dimensions)
Microscopic Analysis
* In this analysis, individual molecular behavior is taken into consideration
¢ This approach is valid when the system becomes rare
(Mean free path of the molecules is of the order of system dimensions)

## Slide 8
PRESSURE GASES * Pressure in gases is due to forces occuring because of colliding molecules with the surface & it acts
normal to tRe surface.
* Pressure is a function of density & temperature
* Density is directly proportional to the number of molecules colliding
* Colliding velocity is directly proportional to temperature.
© |3RT
ms = | {7
{ M
LIQUID ¢ Pressure in the liquid is due to repulsion between molecules.

## Slide 9
THERMODYNAMIC EQUILIBRIUM
>THERMAL EQUILIBRIUM
Equality of temperatures
>» MECHANICAL EQUILIBRIUM
Equality of forces
>» CHEMICAL EQUILIBRIUM
Chemical composition should not change with time
> PHASE EQUILIBRIUM
Mass of each phase should remain constant with time